RS Lambda dimensions

RS Lamba
Dimensions-mm / Chain No. Pitch P Roller Dia. R Width between Roller Link Plates W / Standard Nickel Plated / RSD40-Λ RSD40NP-Λ 12.70 7.92 7.55 / RSD50-Λ RSD50NP-Λ 15.875 10.16 9.26 / RSD60-Λ RSD60NP-Λ 19.05 11.91 12.28 / RSD80-Λ RSD80NP-Λ 25.40 15.88 15.48 / RSD100-Λ RSD100NP-Λ 31.75 19.05 18.70 / RSD120-Λ RSD120NP-Λ 38.10 22.23 24.75 / RSD140-Λ RSD140NP-Λ 44.45 25.40 24.75
Dimensions-mm / Chain No. Link Plate / Standard Nickel Plated Thickness T1 Thickness T2 Height H Height h / RSD40-Λ RSD40NP-Λ 1.5 2.0 12.0 10.4 / RSD50-Λ RSD50NP-Λ 2.0 2.4 15.0 13.0 / RSD60-Λ RSD60NP-Λ 2.4 3.2 18.1 15.6 / RSD80-Λ RSD80NP-Λ 3.2 4.0 24.1 20.8 / RSD100-Λ RSD100NP-Λ 4.0 4.8 30.1 26.0 / RSD120-Λ RSD120NP-Λ 4.8 5.6 36.2 31.2 / RSD140-Λ RSD140NP-Λ 5.6 6.4 42.2 36.4 / Dimensions-mm / Chain No. Pin / Standard Nickel Plated Dia. D From Pin Head to C.L. L1 From Pin end to C.L. L2 From Pin end to C.L. L / RSD40-Λ RSD40NP-Λ 3.97 8.78 10.45 20.0 / RSD50-Λ RSD50NP-Λ 5.09 10.75 12.45 24.0 / RSD60-Λ RSD60NP-Λ 5.96 13.75 15.65 32.0 / RSD80-Λ RSD80NP-Λ 7.94 17.15 20.25 39.9 / RSD100-Λ RSD100NP-Λ 9.54 20.65 23.85 47.5 / RSD120-Λ RSD120NP-Λ 11.11 25.75 29.95 59.0 / RSD140-Λ RSD140NP-Λ 12.71 27.70 32.20 63.7 / Dimensions-mm / Chain No. Average Tensile Strength kN {kgf} Maximum Allowable Load kN {kgf} / Standard Nickel Plated Standard Nickel Plated / RSD40-Λ RSD40NP-Λ 19.1 {1,950} 3.63 {370} 3.04 {310} / RSD50-Λ RSD50NP-Λ 31.4 {3,200} 6.37 {650} 5.39 {550} / RSD60-Λ RSD60NP-Λ 44.1 {4,500} 8.83 {900} 7.26 {740} / RSD80-Λ RSD80NP-Λ 78.5 {8,000} 14.7 {1,500} 12.7 {1,300} / RSD100-Λ RSD100NP-Λ 118 {12,000} 22.6 {2,300} 19.1 {1,950} / RSD120-Λ RSD120NP-Λ 167 {17,000} 30.4 {3,100} 25.5 {2,600} / RSD140-Λ RSD140NP-Λ 216 {22,000} 40.2 {4,100} 34.3 {3,500} / Dimensions-mm / Chain No. Approx. Mass kg/m Number of Links per unit Max. Allowable Chain Speed m/min. / Standard Nickel Plated / RSD40-Λ RSD40NP-Λ 0.70 240 150 / RSD50-Λ RSD50NP-Λ 1.11 192 135 / RSD60-Λ RSD60NP-Λ 1.72 160 120 / RSD80-Λ RSD80NP-Λ 2.77 120 90 / RSD100-Λ RSD100NP-Λ 4.30 96 80 / RSD120-Λ RSD120NP-Λ 6.40 80 50 / RSD140-Λ RSD140NP-Λ 8.10 68 50